## Slide 1
KI-RnB ABS
Roller Bench Test Sequence
LX3 Driving Curve | 33 Steps | 167 sec | Max 100 km/h
ECU INIT
DTC
WSS
SPEED
BRAKE/ABS
PARKING
FINISH
System Legend:
ECU
Diagnostic Communication
PLC
Machine & Roller Control
NI
Sensor Data Acquisition

## Slide 2
PROCESS FLOW
Full sequence: 33 steps in 6 phases
ECU
PLC
NI
PHASE 1 ECU INITIALIZE
0~26s
01
INITIALIZATION
3s
PLC
02
ECU CONNECT
3s
ECU
03
START COMM
5s
ECU
04
ECU IDENT
3s
ECU
05
CHECK SIGNAL
3s
ECU
06
DTC READ
3s
ECU
07
DTC CLEAR
3s
ECU
08
[N] STOP
3s
PLC
PHASE 2 WSS TEST
26~46s
09
WSS READY
4s | 5 km/h
PLC
NI
10
WSS TEST
10s | 5 km/h
ECU
PLC
NI
11
[N] STOP
3s
PLC
12
MODE CHECK
3s
ECU
PHASE 3 SPEED & CRUISE
46~101s
13
SPEED UP
10s | 40 km/h
PLC
NI
14
SMT TEST
5s | 40 km/h
ECU
PLC
NI
15
CRUISE UP
10s | 80 km/h
PLC
NI
16
CRUISE CHECK
20s | 80 km/h
ECU
PLC
NI
17
MAX SPEED
10s | 100 km/h
PLC
NI
PHASE 4 BRAKE & ABS
101~126s
18
ENGINE BRAKE
10s | 90 km/h
PLC
NI
19
DRAG TEST
3s | 80 km/h
PLC
NI
20
BRAKE TEST
3s | 60 km/h
PLC
NI
21
DYNAMIC READY
2s | 55 km/h
PLC
NI
22
DYNAMIC TEST
4s | 10 km/h
ECU
PLC
NI
23
[N] STOP
3s
PLC
PHASE 5 REVERSE & PARKING
126~149s
24
REVERSE [R]
5s
PLC
25
[R] 5KPH
5s | 5 km/h
PLC
NI
26
[N] STOP
3s
PLC
27
PARKING READY
5s
PLC
28
PARKING TEST
5s
PLC
NI
PHASE 6 FINISH
149~167s
29
IDLE
3s
ECU
30
DTC READ
4s
ECU
31
DTC CLEAR
3s
ECU
32
ECU DISCONNECT
3s
ECU
33
FINISH
5s
PLC

## Slide 3
SPEED PROFILE
Vehicle speed over time (167 seconds)
0
20
40
60
80
100
0s
10s
20s
30s
40s
50s
60s
70s
80s
90s
100s
110s
120s
130s
140s
150s
160s
170s
ECU INIT
WSS
SPEED & CRUISE
BRAKE & ABS
REVERSE & PARKING
FINISH
WSS 5km/h
SMT 40km/h
CRUISE 80km/h
MAX 100km/h
DRAG 80km/h
BRAKE 60km/h
ABS DYNAMIC
REVERSE 5km/h
km/h

## Slide 4
PHASE DETAIL
Step-by-step breakdown with timing, speed, system, and description
ECU
PLC
NI
PHASE 1
ECU INITIALIZE
0-26s | 26s
#
STEP
TIME
km/h
SYSTEM
NOTE
01
INITIALIZATION
3s
-
PLC
System boot
02
ECU CONNECT
3s
-
ECU
Diagnostic link
03
START COMM
5s
-
ECU
UDS session start
04
ECU IDENT
3s
-
ECU
ECU version read
05
CHECK SIGNAL
3s
-
ECU
Brake switch check
06
DTC READ
3s
-
ECU
Read fault codes
07
DTC CLEAR
3s
-
ECU
Clear fault codes
08
[N] STOP
3s
-
PLC
Neutral stop
PHASE 2
WSS TEST
26-46s | 20s
#
STEP
TIME
km/h
SYSTEM
NOTE
09
WSS READY
4s
5
PLC
NI
Roll start
10
WSS TEST
10s
5
ECU
PLC
NI
4-wheel speed check
11
[N] STOP
3s
-
PLC
Neutral stop
12
MODE CHECK
3s
-
ECU
Drive mode verify
PHASE 3
SPEED & CRUISE
46-101s | 55s
#
STEP
TIME
km/h
SYSTEM
NOTE
13
SPEED UP
10s
40
PLC
NI
Accelerate to 40
14
SMT TEST
5s
40
ECU
PLC
NI
Speedometer check
15
CRUISE UP
10s
80
PLC
NI
Accelerate to 80
16
CRUISE CHECK
20s
80
ECU
PLC
NI
Cruise control test
17
MAX SPEED
10s
100
PLC
NI
Max speed test
PHASE 4
BRAKE & ABS
101-126s | 25s
#
STEP
TIME
km/h
SYSTEM
NOTE
18
ENGINE BRAKE
10s
90
PLC
NI
Engine braking
19
DRAG TEST
3s
80
PLC
NI
Rolling resistance
20
BRAKE TEST
3s
60
PLC
NI
Base brake force
21
DYNAMIC READY
2s
55
PLC
NI
Pedal release
22
DYNAMIC TEST
4s
10
ECU
PLC
NI
ABS reduction/recovery
23
[N] STOP
3s
-
PLC
Neutral stop
PHASE 5
REVERSE & PARKING
126-149s | 23s
#
STEP
TIME
km/h
SYSTEM
NOTE
24
REVERSE [R]
5s
-
PLC
Shift to reverse
25
[R] 5KPH
5s
5
PLC
NI
Reverse speed check
26
[N] STOP
3s
-
PLC
Neutral stop
27
PARKING READY
5s
-
PLC
Parking brake pull
28
PARKING TEST
5s
-
PLC
NI
Parking brake hold
PHASE 6
FINISH
149-167s | 18s
#
STEP
TIME
km/h
SYSTEM
NOTE
29
IDLE
3s
-
ECU
Idle stability
30
DTC READ
4s
-
ECU
Final fault check
31
DTC CLEAR
3s
-
ECU
Clear fault codes
32
ECU DISCONNECT
3s
-
ECU
Close session
33
FINISH
5s
-
PLC
Test complete